Таймер в автомобиль U6046B - УР1101ХП16

Для таймеров автомобилей существуют СПЕЦИАЛЬНЫЕ микросхемы. Atmel u6046b. Два типа корпусов. Эту микросхему можно купить на Алиэкспрессе.
Есть несколько аналогов. Российский полный аналог УР1101ХП16.
Для россиян удобнее купить ГОТОВОЕ реле на УР1101ХП16. 
Реле называется 456.3747-02
Это в пластмассовом корпусе сама УР1101ХП16 со схемой управления и электромагнитным реле на выходе. Цена этого реле разная у разных продавцов, мне в Москве удалось купить за 145 руб.
А корейское реле на оригинале (u6046b) называется 96116223. Тоже можно купить, но это подороже. Схема у российского реле один в один, как у корейского и соответствует даташиту на u6046b.

Features

• Delay Time Range: 3.7s to 20h

• RC Oscillator Determines Timing Characteristics

• Relay Driver with Z-diode

• Debounced Input for Toggle Switch

• Two Debounced Inputs: ON and OFF

• Load-dump Protection

• RF Interference Protected

• Protection According to ISO/TR7637-1 (VDE 0839)

• Inputs Switched to VBatt

- Description

The bi-polar long-term timer U6046B is designed to automatically limit the operation time of high loads in the harsh automotive environment with a preset delay time. With the power-on-reset function the timers guarantee that current consuming devices are not operated unintentionally. The delay time can be interrupted manually, but a retrigger function is not provided.