7 Detailed Description

7.1 Overview

The TPA31xxD2 device is a highly efficient Class D audio amplifier with integrated 120m Ohms MOSFET that

allows output currents up to 7.5 A. The high efficiency allows the amplifier to provide an excellent audio

performance without the need for a bulky heat sink.

The device can be configured for either master or slave operation by using the SYNC pin. This helps to prevent

audible beats noise.

7.3 Feature Description

7.3.1 Gain Setting and Master and Slave

The gain of the TPA31xxD2 family is set by the voltage divider connected to the GAIN/SLV control pin. Master or

Slave mode is also controlled by the same pin. An internal ADC is used to detect the 8 input states. The first four

stages sets the GAIN in Master mode in gains of 20, 26, 32, 36 dB respectively, while the next four stages sets

the GAIN in Slave mode in gains of 20, 26, 32, 36 dB respectively. The gain setting is latched during power-up

and cannot be changed while device is powered. Table 1 lists the recommended resistor values and the state

and gain:

| In Master mode, SYNC terminal is an output, in Slave mode, SYNC terminal is an input for a clock input. TTL logic levels with compliance to GVDD. |  |
| --- | --- |

7.3.11 Thermal Protection

Thermal protection on the TPA31xxD2 family prevents damage to the device when the internal die temperature

exceeds 150°C. There is a ±15°C tolerance on this trip point from device to device. Once the die temperature

exceeds the thermal trip point, the device enters into the shutdown state and the outputs are disabled. This is a

latched fault.

Thermal protection faults are reported on the FAULTZ terminal as a low state.

If automatic recovery from the thermal protection latch is desired, connect the FAULTZ pin directly to the SDZ

pin. This allows the FAULTZ pin function to automatically drive the SDZ pin low which clears the thermal

protection latch.

7.3.12 Device Modulation Scheme

The TPA31xxD2 family has the option of running in either BD modulation or 1SPW modulation; this is set by the

MODSEL pin.

7.3.12.1 MODSEL = GND: BD-Modulation

This is a modulation scheme that allows operation without the classic LC reconstruction filter when the amp is

driving an inductive load with short speaker wires. Each output is switching from 0 volts to the supply voltage.

The OUTPx and OUTNx are in phase with each other with no input so that there is little or no current in the

speaker. The duty cycle of OUTPx is greater than 50% and OUTNx is less than 50% for positive output voltages.

The duty cycle of OUTPx is less than 50% and OUTNx is greater than 50% for negative output voltages. The

voltage across the load sits at 0V throughout most of the switching period, reducing the switching current, which

reduces any I2R losses in the load.

7.3.12.2 MODSEL = HIGH: 1SPW-modulation

The 1SPW mode alters the normal modulation scheme in order to achieve higher efficiency with a slight penalty

in THD degradation and more attention required in the output filter selection. In 1SPW mode the outputs operate

at ~15% modulation during idle conditions. When an audio signal is applied one output will decrease and one will

increase. The decreasing output signal will quickly rail to GND at which point all the audio modulation takes place

through the rising output. The result is that only one output is switching during a majority of the audio cycle.

Efficiency is improved in this mode due to the reduction of switching losses. The THD penalty in 1SPW mode is

minimized by the high performance feedback loop. The resulting audio signal at each half output has a

discontinuity each time the output rails to GND. This can cause ringing in the audio reconstruction filter unless

care is taken in the selection of the filter components and type of filter used.

7.3.13 Efficiency: LC Filter Required with the Traditional Class-D Modulation Scheme

The main reason that the traditional class-D amplifier-based on AD modulation needs an output filter is that the

switching waveform results in maximum current flow. This causes more loss in the load, which causes lower

efficiency. The ripple current is large for the traditional modulation scheme, because the ripple current is

proportional to voltage multiplied by the time at that voltage. The differential voltage swing is 2 × VCC, and the

time at each voltage is half the period for the traditional modulation scheme. An ideal LC filter is needed to store

the ripple current from each half cycle for the next half cycle, while any resistance causes power dissipation. The

speaker is both resistive and reactive, whereas an LC filter is almost purely reactive.

The TPA3116D2 modulation scheme has little loss in the load without a filter because the pulses are short and

the change in voltage is VCC instead of 2 × VCC. As the output power increases, the pulses widen, making the

ripple current larger. Ripple current could be filtered with an LC filter for increased efficiency, but for most

applications the filter is not needed.

An LC filter with a cutoff frequency less than the class-D switching frequency allows the switching current to flow

through the filter instead of the load. The filter has less resistance but higher impedance at the switching

frequency than the speaker, which results in less power dissipation, therefore increasing efficiency.

7.3.14 Ferrite Bead Filter Considerations

Using the Advanced Emissions Suppression Technology in the TPA3116D2 amplifier it is possible to design a

high efficiency class-D audio amplifier while minimizing interference to surrounding circuits. It is also possible to

accomplish this with only a low-cost ferrite bead filter. In this case it is necessary to carefully select the ferrite

bead used in the filter. One important aspect of the ferrite bead selection is the type of material used in the ferrite

bead. Not all ferrite material is alike, so it is important to select a material that is effective in the 10 to 100 MHz

range which is key to the operation of the class-D amplifier. Many of the specifications regulating consumer

electronics have emissions limits as low as 30 MHz. It is important to use the ferrite bead filter to block radiation

in the 30 MHz and above range from appearing on the speaker wires and the power supply lines which are good

antennas for these signals. The impedance of the ferrite bead can be used along with a small capacitor with a

value in the range of 1000 pF to reduce the frequency spectrum of the signal to an acceptable level. For best

performance, the resonant frequency of the ferrite bead/ capacitor filter should be less than 10 MHz.

Also, it is important that the ferrite bead is large enough to maintain its impedance at the peak currents expected

for the amplifier. Some ferrite bead manufacturers specify the bead impedance at a variety of current levels. In

this case it is possible to make sure the ferrite bead maintains an adequate amount of impedance at the peak

current the amplifier will see. If these specifications are not available, it is also possible to estimate the bead

current handling capability by measuring the resonant frequency of the filter output at low power and at maximum

power. A change of resonant frequency of less than fifty percent under this condition is desirable. Examples of

ferrite beads which have been tested and work well with the TPA3130D2 can be seen in the TPA3130D2EVM

user guide SLOU341.

A high quality ceramic capacitor is also needed for the ferrite bead filter. A low ESR capacitor with good

temperature and voltage characteristics will work best.

Additional EMC improvements may be obtained by adding snubber networks from each of the class-D outputs to

ground. Suggested values for a simple RC series snubber network would be 18 Ω in series with a 330 pF

capacitor although design of the snubber network is specific to every application and must be designed taking

into account the parasitic reactance of the printed circuit board as well as the audio amp. Take care to evaluate

the stress on the component in the snubber network especially if the amp is running at high PVCC. Also, make

sure the layout of the snubber network is tight and returns directly to the GND pins on the IC.

7.3.15 When to Use an Output Filter for EMI Suppression

The TPA3116D2 has been tested with a simple ferrite bead filter for a variety of applications including long

speaker wires up to 125 cm and high power. The TPA3116D2 EVM passes FCC class-B specifications under

these conditions using twisted speaker wires. The size and type of ferrite bead can be selected to meet

application requirements. Also, the filter capacitor can be increased if necessary with some impact on efficiency.

There may be a few circuit instances where it is necessary to add a complete LC reconstruction filter. These

circumstances might occur if there are nearby circuits which are sensitive to noise. In these cases a classic

second order Butterworth filter similar to those shown in the figures below can be used.

Some systems have little power supply decoupling from the AC line but are also subject to line conducted

interference (LCI) regulations. These include systems powered by "wall warts" and "power bricks." In these

cases, LC reconstruction filters can be the lowest cost means to pass LCI tests. Common mode chokes using

low frequency ferrite material can also be effective at preventing line conducted interference.

| 7.4.1 Mono Mode (PBTL) The TPA31xxD2 family can be connected in MONO mode enabling up to 100W output power. This is done by: • Connect INPL and INNL directly to Ground (without capacitors) this sets the device in Mono mode during power up. • Connect OUTPR and OUTNR together for the positive speaker terminal and OUTNL and OUTPL together for the negative pin. • Analog input signal is applied to INPR and INNR. |  |
| --- | --- |

8.2.2 Detailed Design Procedure

The TPA31xxD2 family is a very flexible and easy to use Class D amplifier; therefore the design process is

straightforward. Before beginning the design, gather the following information regarding the audio system.

• PVCC rail planned for the design

• Speaker or load impedance

• Maximum output power requirement

• Desired PWM frequency

8.2.2.1 Select the PWM Frequency

Set the PWM frequency by using AM0, AM1 and AM2 pins.

8.2.2.2 Select the Amplifier Gain and Master/Slave Mode

In order to select the amplifier gain setting, the designer must determine the maximum power target and the

speaker impedance. Once these parameters have been determined, calculate the required output voltage swing

which delivers the maximum output power.

Choose the lowest analog gain setting that corresponds to produce an output voltage swing greater than the

required output swing for maximum power. The analog gain and master/slave mode can be set by selecting the

voltage divider resistors (R1 and R2) on the Gain/SLV pin.

8.2.2.3 Select Input Capacitance

Select the bulk capacitors at the PVCC inputs for proper voltage margin and adequate capacitance to support the

power requirements. In practice, with a well-designed power supply, two 100-μF, 50-V capacitors should be

sufficient. One capacitor should be placed near the PVCC inputs at each side of the device. PVCC capacitors

should be a low ESR type because they are being used in a high-speed switching application.

8.2.2.4 Select Decoupling Capacitors

Good quality decoupling capacitors need to be added at each of the PVCC inputs to provide good reliability,

good audio performance, and to meet regulatory requirements. X5R or better ratings should be used in this

application. Consider temperature, ripple current, and voltage overshoots when selecting decoupling capacitors.

Also, these decoupling capacitors should be located near the PVCC and GND connections to the device in order

to minimize series inductances.

8.2.2.5 Select Bootstrap Capacitors

Each of the outputs require bootstrap capacitors to provide gate drive for the high-side output FETs. For this

design, use 0.22-μF, 25-V capacitors of X5R quality or better.

9 Power Supply Recommendations

The power supply requirements for the TPA3116D2 consist of one higher-voltage supply to power the output

stage of the speaker amplifier. Several on-chip regulators are included on the TPA3116D2 to generate the

voltages necessary for the internal circuitry of the audio path. It is important to note that the voltage regulators

which have been integrated are sized only to provide the current necessary to power the internal circuitry. The

external pins are provided only as a connection point for off-chip bypass capacitors to filter the supply.

Connecting external circuitry to these regulator outputs may result in reduced performance and damage to the

device. The high voltage supply, between 4.5 V and 26 V, supplies the analog circuitry (AVCC) and the power

stage (PVCC). The AVCC supply feeds internal LDO including GVDD. This LDO output are connected to

external pins for filtering purposes, but should not be connected to external circuits. GVDD LDO output have

been sized to provide current necessary for internal functions but not for external loading.