# TP5100 double single lithium battery charge management compatible 2A rechargeable lithium plate

TP5100 is a double switch buck 8.4V, single cell 4. 2V lithium battery charge management chip. Its ultra-compact QFN16 package and simple external circuit, making TP5100 ideal for portable equipment so large current charging management circuit protection, battery temperature monitoring, reverse battery protection.

TP5100 have 5V-18V wide input voltage, dual battery trickle charge into pre-charge, constant current, constant voltage three phase, pre-charge current trickle charge current through an external resistor adjustment, the maximum charge current up to 2A. TP5100 with a frequency of 400kHz switching mode makes it possible to use a smaller outer Suo device and the large current charging still maintain a smaller amount of heat.

TP51OO built-in power PMOSFET, anti-intrusion circuit, so no anti-intrusion protection and other external Schottky diode.

Features:

- Double 8.4v / 4.2v lithium rechargeable single

- Programmable charge current. 0. 1A-2A

- Programmable steady precharge current 10% -100%.

- Wide operating voltage, maximum reach I8V

- Red and green LED charge status indicator

- Chip temperature protection, overcurrent protection, undervoltage protection

- Battery temperature protection, reverse battery shutdown, short circuit protection

- Switching frequency 400Khz, usable inductance 20uH and more

- PWR_ON Power battery for switching control

Maximum Ratings:

- Static input supply voltage (VlN): 20V

- BAI: -8.4V-20V

- BAT Short-Circuit Duration: Continuous

- Operating environment Temperature range: -40 ° -85 °

- Storage temperature range: -65 ° - 125 °

Application:

- Portable equipment, various chargers

- Smartphone, PDA, mobile cellular telephone

- MP4, MP5 players, tablets

- HM

- Power Tools

- Walkie-talkie

Default shipping settings: 4.2V 2A. The board has with LED, and LED's external reserve position.

Size: 25 * 17 * 5mm ultra-small size

Input voltage: 5-18V DC power supply

Charge status: full and unloaded blue lights, charging red.

Package Included:

1PCS*TP5100 2 cells / single Lithium Lion Battery Charger Module 2A 18650 Charging PCB

Напряжение полного заряда для 1-й Li-Ion батареи - 4.2V.

Входное напряжение - от 5 до 15VDC.

Напряжение полного заряда для 2-х, последовательно включенных, Li-Ion батарей - 8.4V.

Входное напряжение - от 10 до 15VDC.

Ток заряда - 2A  (необходимо приклеить радиатор с обратной стороны платы).

При токе заряда 1А - радиатор не нужен, но необходимо выпаять один из двух резисторов с маркировкой "R100".

По умолчанию выставлен режим заряда 1-й Li-Ion батареи.

При необходимости заряжать две Li-Ion батареи, впаяйте перемычку между контактами "SET".

На плате установлены синий и красный светодиоды.

Если горит синий - нет батареи или заряд окончен.

Если горит красный - идёт зарядка.

При необходимости можно установить внешний вдухцветный светодиод.

TP5100 lithium ion battery is 8.4V 1.5A double charge (precharge 150MA) Application schematic