ME2108_DC-DC Step up 1V to 5V Краткое изложение даташита.

Вместо NPN можно использовать N-MOS транзистор AAT9460、XP151、XP161 с прямым подключением затвора к ИС.

| Operation： ME2108 step-up DC/DC converter charges energy in the inductor when Lx Transistor is on, and discharges the energy with the addition of the energy from input power source thereto, so that a higher output voltage than the input voltage is obtained. Following is the operation diagram. |  |
| --- | --- |

Selection of Peripheral Components and Application Notes

Peripheral components should be selected carefully because they are greatly affect the performances of

ME2108：

Ø Use capacitor with a capacity of 10μF or more ( too small capacity will lead to high output ripple),

and with good frequency characteristics ( it is better to use Tantalum type). Besides, it is

recommended the use of a capacitor with an allowable voltage which is at least three times the

output set voltage. This is because there may be the case where a spike-shaped high voltage is

generated by the inductor when Lx transistor is turned OFF.

Ø Choose such an inductor that has sufficiently small d.c. resistance and large allowable current, and

hardly reaches magnetic saturation. When the inductance value of the inductor is small, there may

be the case where ILX exceeds the absolute maximum ratings at the maximum load.

Ø Use a diode of a Schottky type with high switching speed.