- Fast, Wide Range, Discrete Function Generator

http://webpages.charter.net/dawill/tmoranwms/Circuits_2008/index.html

Thanks to the high bias current and overall simplicity (only five transistors and two diodes in the functional loop), this triangle wave generator is able to run very fast. With Ct = 0 and the circuit breadboarded, this circuit runs at over 30MHz. With Ct = 680pF and room temperature about 60°F, it was found adjustable from 1Hz to 4.5MHz in one range. Linearity is excellent with sufficient capacitance (Ct > 200pF or so). The squarewave at the 2N4403 collector has rise/fall times on the order of 20ns.

2N4403 – КТ644Б, 2N4401-КТ603Б (КТ602), 2N3904-КТ340В(КТ342Б)

- Function Generator

A typical function generator circuit, this consists of a current mirror (the top mirror sends double current to the bottom mirror), JFET follower, differential hysteretic comparator and an output buffer. A triangle wave is seen at JFET source, which can be trimmed into a sine wave, hence this is a function generator.

ГенераторФункциональный_start7218

Подробно Радио №11 1980 стр 44., Радиоежегодник 1983 стр. 190

Спасибо коллеги за помощь! Только что запустил свой экземпляр с пол пинка! Качество сигналов даже удивило, отличные меандр и пила, и не плохой синус. Стабильность очень даже не плохая. Вогнал частоты от 20Гц до 500кГц с разбитием на 4 диапазона безо всяких проблем...Сейчас придет коллега со своим экземпляром и будем разбираться...приведенные мной осциллограммы имеют тот же вид в пределах частот от 20 Гц до 500 кГц, единственное что есть так это то что на частотах выше 200 кГц (что явно выше заявленного производителем) синус имеет на пиках не большие "гармошки" которые существенно ослабляются заменой С10 на 2,2Н, чтоб не усложнять фильтрами. Результат на 101% совпадает со всеми заявленными характеристиками.

ТТЛ инвертор с открытым коллектором – ЛН5 (вместо ЛА8 – тоже с ОК)См. так же 1533ЛА8/ Другие ИС с ОК – ЛА7…ЛА11, ЛА13, ЛА18, ЛИ2, ЛИ4, ЛИ5

|  |  | Оптимальное сопротивление резистора R2 (при котором передаточная функции усилителя наиболее близка к синусоидальной ) можно найти по приближенной формуле R =2Uт/Iк. |
| --- | --- | --- |