# Blutooth 4_2 CSRA64215 APTXLL Lossless

Blutooth аудио модуль, обладающий массой преимуществ:
- поддерживает aptX и ААС кодеки,
- на борту гальваническая развязка по питанию (вход 5 или 12 В на выбор),
- на борту отличный малошумящий усилитель для наушников,
- одновременая работа с двумя смартфонами/планшетами,
- возможность питания напрямую от Li-Ion аккума,
- 10-типолосный эквалайзер, 
- встроенный контроллер зарядки аккума,
- можно поменять имя устройства.

Купить на Aliexpress -> http://ali.pub/31o02d $12.23

Почти у всех блютуз модулей управление эквалайзером и другими фишками только через прогер...

на миску есть рецепт как подключить к этому модулю FTDI программатор за 2 бакса. И собственно как все настроить

или через приложение на Андроид: GAIA Control (его нет на плэймаркете, но легко гуглится)

# Mini MP3 Bluetooth 4.1 Lossless Decoder Stereo Output Board Car Speaker Amplifier Module Circuit Board Module 3.7V 5V Micro Usb

https://ru.aliexpress.com/item/Mini-MP3-Bluetooth-4-1-Lossless-Decoder-Stereo-Output-Board-Car-Speaker-Amplifier-Module-Circuit-Board/32885652652.html?spm=a2g0v.10010108.1000016.1.2fba5ea4FptTQm&isOrigTitle=true

Bluetooth 4.1 support, support for automatic connection, WAV+APE+FLAC+MP3 lossless decoding, stereo output.

1.Parameter characteristics

| Power Supply | 3.7-5V |
| --- | --- |
| SNR | 90dB |
| THD+N | -70dB |
| Crosstalk | -86dB |
| DNR | 91dB |
| Support Profile | A2DP/AVCTP/AVDTP/AVRCP/HFP |
| LOS | >15m |

2.Interface details

USB powered 
 Universal Micro USB 5V power supply 
 
3.7-5V Supply Pad 
 External 3.7-5V lithium battery power conversion 
 
LED indicator 
 Bluetooth mode long blue light 
 
3.5mm stereo audio interface 
 Standard 3.5mm interface, output stereo

Instructions:

After the power is turned on, the blue indicator lights up and enters the Bluetooth mode; the English “The bluetooth device is ready to pair” is displayed, indicating that the Bluetooth mode is entered and waiting for pairing; the “XY_BT” searched by the mobile phone Bluetooth is the device name of the decoding board. , Click on the connection, the decoder board prompts "The bluetooth device is connected successfully", indicating that the decoder board and the mobile phone are connected successfully, you can play music. As shown below

Package Contents:

1X 3.7-5V Mini Bluetooth MP3 Decoder Board Power amplifier Board Bluetooth 4.1